GPU计算与工程应用
王银沼 22021071
实验环境：
CPU inter i9-10900k
GPU rtx 2080ti
操作系统 manjaro(linux)

实验内容
利用GPU加速三角形的碰撞检测，包括两个物体之间的碰撞和物体的自碰撞检测

实验原理：
使用cpu进行三角形的碰撞检测时，无论是物体间还是物体自身，都需要用到双层循环进行，如物体间碰撞检测，需要对依次判断物体a上每个三角形与物体b上每个三角形之间的碰撞情况，而每一次判断之间，都是相互独立的，所以可以利用并行算法进行加速。在cpu端，可以使用openmp库，充分利用cpu的多核，进行一定程序上的并行加速。这样的加速受限于cpu的核数，但一般cpu最多的核数也就几十个，完全无法充分实现并行算法的效率，所以使用超多核心的gpu可以显著提升效率。
实验思路：
物体间碰撞
方案一：
对于两个进行碰撞检测的物体a和b，选取三角形数量比较多的物体作为物体a。一个block负责一个物体a的三角形与所有物体b三角形的碰撞检测，所以kernel函数的block个数设为物体a三角形的个数，且为一维。一个block设置threads_per_block个线程，假设每个线程的id为tid，则该线程负责的物体b的三角形编号为tid+i*threads_per_block，其中i表示第i次循环，共需要次数pass为：
pass=(num_tri_of_b+threads_per_block-1)/threads_per_block

预先设置好每个三角形最多的碰撞个数，那么可以在kernerl启动前分配好显存，在kernel执行过程中将碰撞结果写到显存中，最后传回结果到cpu内存即可。

 __global__ void cuTriContactDetect_v0(tri3f* a_tris,tri3f* b_tris,
        vec3f* a_vtxs,vec3f* b_vtxs,
        uint a_tris_num,uint b_tris_num,
        uint* res)
{
    __shared__ uint contacted[threads_per_block];
    __shared__ uint cur_contact_num;
    __shared__ Lock lock;
    cur_contact_num=0;
    int gid=threadIdx.x+blockIdx.x*blockDim.x;
    int bid=blockIdx.x;
    int tid=threadIdx.x;
    if (tid==0) lock.init();
    contacted[tid]=0;
    int pass=(b_tris_num+threads_per_block-1)/threads_per_block;
    uint a_tri_x=a_tris[bid].id(0);
    uint a_tri_y=a_tris[bid].id(1);
    uint a_tri_z=a_tris[bid].id(2);
    vec3f a_vtx_x=a_vtxs[a_tri_x];
    vec3f a_vtx_y=a_vtxs[a_tri_y];
    vec3f a_vtx_z=a_vtxs[a_tri_z];
    __syncthreads();
    for(int i=0;i<pass;i++){
        int idx=tid+i*threads_per_block;
        if(idx<b_tris_num){
        uint p_x=b_tris[idx].id(0);
        uint p_y=b_tris[idx].id(1);
        uint p_z=b_tris[idx].id(2);
        vec3f b_vtx_x=b_vtxs[p_x];
        vec3f b_vtx_y=b_vtxs[p_y];
        vec3f b_vtx_z=b_vtxs[p_z];
        if(cuTriContact(a_vtx_x,a_vtx_y,a_vtx_z,b_vtx_x,b_vtx_y,b_vtx_z)){
        lock.lock();
        if (cur_contact_num<threads_per_block){
        contacted[cur_contact_num]=idx;
        cur_contact_num++;
        }
        lock.unlock();
        }
        }
        __syncthreads();
    }
        if (tid==0){
        res[bid*threads_per_block]=cur_contact_num;
        }
        if(tid<cur_contact_num && tid<threads_per_block-1)
        res[gid+1]=contacted[tid];
}
方案二：
一个block里的每一个线程负责一个物体a的三角形与物体b所有三角形的碰撞检测。假设一个block里有threads_per_block个线程，那么一个block需加载这么多个相应物体a的三角形，以及每一次pass需要加载相同个数的物体b的三角形。但是每次加载的threads_per_block个物体b的三角形，每一个物体a的三角形都需要用到，所以可以将这部分三角形存到shared内存中。
对于threads_per_block个物体a和物体b的三角形，每一个物体a的三角形需要与这部分物体b的三角形进行碰撞检测，这可以通过一个循环配对实现:
第i次，三角形a(j)与三角形b((j+i)%threads_per_block)进行配对检测，只需要进行threads_per_block次即可，然后进行下一次的pass，其余部分与方案一相同。

    __global__ void cuTriContactDetect_v1(tri3f* a_tris,tri3f* b_tris,
        vec3f* a_vtxs,vec3f* b_vtxs,
        uint a_tris_num, uint b_tris_num,
        uint* res)
{
    __shared__ uint contact_num[threads_per_block];
    __shared__ uint contacted[threads_per_block][8];
    uint32_t gid=threadIdx.x+blockIdx.x*blockDim.x;
    uint32_t bid=blockIdx.x;
    uint32_t tid=threadIdx.x;
    uint32_t pass=(b_tris_num+threads_per_block-1)/threads_per_block;
    //read a tris from global memory
    tri3f a_tri_id=a_tris[gid];
    vec3f a_vtx_0=a_vtxs[a_tri_id.id0()];
    vec3f a_vtx_1=a_vtxs[a_tri_id.id1()];
    vec3f a_vtx_2=a_vtxs[a_tri_id.id2()];
    contact_num[tid]=0;
    __syncthreads();
    for(uint32_t i=0;i<pass;i++){
        uint pass_t=i*threads_per_block;
        uint idx=tid+pass_t;
        __shared__ double cache_b_tris[threads_per_block][9];
        tri3f b_tri_id=b_tris[idx];
        vec3f b_vtx_0=b_vtxs[b_tri_id.id0()];
        vec3f b_vtx_1=b_vtxs[b_tri_id.id1()];
        vec3f b_vtx_2=b_vtxs[b_tri_id.id2()];
        cache_b_tris[tid][0]=b_vtx_0.x;
cache_b_tris[tid][1]=b_vtx_0.y;
cache_b_tris[tid][2]=b_vtx_0.z;
        cache_b_tris[tid][3]=b_vtx_1.x;
cache_b_tris[tid][4]=b_vtx_1.y;
cache_b_tris[tid][5]=b_vtx_1.z;
        cache_b_tris[tid][6]=b_vtx_2.x;
cache_b_tris[tid][7]=b_vtx_2.y;
cache_b_tris[tid][8]=b_vtx_2.z;
        for(uint32_t j=0;j<threads_per_block;j++){
        uint32_t idx_=(tid+j)%threads_per_block;
        vec3f b_vtx_0_{cache_b_tris[idx_][0],cache_b_tris[idx_][1],cache_b_tris[idx_][2]};
        vec3f b_vtx_1_{cache_b_tris[idx_][3],cache_b_tris[idx_][4],cache_b_tris[idx_][5]};
        vec3f b_vtx_2_{cache_b_tris[idx_][6],cache_b_tris[idx_][7],cache_b_tris[idx_][8]};
        if(cuTriContact(a_vtx_0,a_vtx_1,a_vtx_2,b_vtx_0_,b_vtx_1_,b_vtx_2_)){
        contacted[tid][contact_num[tid]++]=pass_t+idx_;
        }
        //no need sync?
        }
        __syncthreads();
    }
    res[gid*threads_per_block]=contact_num[tid];
    for(uint32_t i=0;i<contact_num[tid];i++){
        res[gid*threads_per_block+i+1]=contacted[tid][i];
    }
}
方案三：
方案一和方案二都是以顶点数据和顶点索引的形式存储三角形，这样子可以减少重复顶点的冗余存储，但是每次访问三角形的顶点数据时，都需要先获得三个顶点每个的索引，然后根据索引获取实际顶点数据，相当于多了一倍的全局内存访问时间，因此可以只存储顶点数据，减少访问全局内存的时间，但是相应的内存需求或增大。该方案其他思路没有变化，最后实验发现时间也基本相同。
物体自碰撞
方案一：
总体上思路与物体间碰撞方案一的思路类似，唯一不同的是一个三角形如果与所有三角形都进行碰撞检测，那么就会多一次重复测试，所以对于每个三角形，只与比它序号大的三角形进行碰撞检测即可。

__global__ void cuTriContactDetect_self_v0(tri3f* a_tris,vec3f* a_vtxs,uint a_tris_num,uint* res)
{
    __shared__ uint contact_num;
    __shared__ uint contacted[MAX_CONTACT_NUM];
    __shared__ Lock lock;
    uint32_t gid=threadIdx.x+blockIdx.x*blockDim.x;
    uint32_t bid=blockIdx.x;
    uint32_t tid=threadIdx.x;
// printf("kernel\n");
    tri3f a_tri_id=a_tris[bid];
    vec3f a_vtx_0=a_vtxs[a_tri_id.id0()];
    vec3f a_vtx_1=a_vtxs[a_tri_id.id1()];
    vec3f a_vtx_2=a_vtxs[a_tri_id.id2()];
    if(tid==0){
        contact_num=0;
        lock.init();//不能多次初始化
    }
    uint32_t pass=(a_tris_num+threads_per_block-1)/threads_per_block;
    __syncthreads();
    for(uint32_t i=bid/threads_per_block;i<pass;i++){
        uint32_t idx=tid+i*threads_per_block;
        if(idx>bid && idx<a_tris_num){
        tri3f a_tri_id_=a_tris[idx];
        if(!cuTriAdjacent(a_tri_id,a_tri_id_)){
        vec3f a_vtx_0_=a_vtxs[a_tri_id_.id0()];
        vec3f a_vtx_1_=a_vtxs[a_tri_id_.id1()];
        vec3f a_vtx_2_=a_vtxs[a_tri_id_.id2()];
        if(cuTriContact(a_vtx_0,a_vtx_1,a_vtx_2,a_vtx_0_,a_vtx_1_,a_vtx_2_)){
        lock.lock();
        if(contact_num<MAX_CONTACT_NUM){
        contacted[contact_num]=idx;
        contact_num++;
        }
        lock.unlock();
        }
        }
        }
        __syncthreads();
    }
    if(tid==0)
        res[bid*threads_per_block]=contact_num;
    if(tid<contact_num && tid<MAX_CONTACT_NUM)
        res[gid+1]=contacted[tid];
}
方案二：
利用bvh树进行加速。无论是利用bvh进行物体间还是物体自身碰撞检测，其实都是一样的，所以本实验只实现了旗帜自碰撞的bvh加速。普通bvh树需要在cpu使用递归建立，当然也有适用并行构建的线性bvh（lbvh），本实验因为时间原因只实现了在cpu使用递归建树。将cpu端建立的树上传到gpu端，进行并行加速，所以加速的部分主要是利用bvh树进行碰撞检测。
由于kernel函数中每一个线程负责一个三角形与整棵bvh的碰撞检测，因此如果使用递归，很容易造成kernel函数执行崩溃，故采用堆栈+遍历的方法实现递归，可以保证程序不崩溃，并且提升效率。

__global__ void cuTriContactDetect_bvh_v0(Triangle * tris, BVHNode * root, uint tris_num, uint* res)
{
    uint32_t gid=threadIdx.x+blockIdx.x*blockDim.x;
    uint contact_num=0;
    if(gid<tris_num){
        cuIterativeCD(&tris[gid],root,gid,contact_num,res);
        res[gid*threads_per_block]=contact_num;
    }
}
__device__ void cuIterativeCD(const Triangle *tri, const BVHNode *node, uint gid, uint &contact_num, uint *res)
{
    BVHNode* stack[64];
    uint32_t stack_pos=0;
    stack[stack_pos++]=nullptr;
    Bound3 bound=tri->CuGetBound3();
    const BVHNode* _node=node;
    do{
// _node=nullptr;//ok
        if(_node->IsLeafNode() ){
        if(_node->object_->CuGetID()>tri->CuGetID()){
        auto v_id0=tri->CuGetTriID();
        auto v_id1=_node->object_->CuGetTriID();
        bool is_adj=false;
        for(int i=0;i<3;i++)
        for(int j=0;j<3;j++)
        if(v_id0.id(i)==v_id1.id(j)){
        is_adj=true;
        break;
        }
        if(!is_adj && cuTriContact(tri->CuV0(),tri->CuV1(),tri->CuV2(),_node->object_->CuV0(),_node->object_->CuV1(),_node->object_->CuV2())){
        res[gid*threads_per_block+contact_num+1]=_node->object_->CuGetID();
        contact_num++;
        }
        }
        _node=stack[--stack_pos];
        }
        else{
        auto left=_node->left_;
        auto right=_node->right_;
        bool traverseL=Insect(bound,left->GetBound3());
        bool traverseR=Insect(bound,right->GetBound3());
        _node=(traverseL)?left:right;
        if(traverseL && traverseR)
        stack[stack_pos++]=right;
        }
    }while(_node!=nullptr);
}
实验结果
物体间碰撞检测（kneel-lowres数据）
方案一：
Start cd checking ...
-------------------------------
GPU Native(version 0):
GPU collision detected number is: 1083
GPU collision detected time used: 76 ms
CPU Naive:
CPU collision detected number is: 1083
CPU collision detected time used: 360 ms
-------------------------------
Finish checking: 0.65377 seconds

方案二：

Start cd checking ...
-------------------------------
GPU Native(version 1):
GPU collision detected number is: 1083
GPU collision detected time used: 93 ms
CPU Naive:
CPU collision detected number is: 1083
CPU collision detected time used: 365 ms
-------------------------------
Finish checking: 0.67871 seconds

方案三：
Start cd checking ...
-------------------------------
GPU Native(version 2):
GenerateTrisData
obj a data generate finish...
obj b data generate finish...
generate tris data finish...
GPU collision detected number is: 1083
GPU collision detected time used: 82 ms
CPU Naive:
CPU collision detected number is: 1083
CPU collision detected time used: 356 ms
-------------------------------
Finish checking: 0.63098 seconds
物体自碰撞：
run 1：
Start checking self-CD...
-------------------------------
CPU BVH:
CPU BVH build time taken: 216ms
CPU BVH collision detected number is: 1754
CPU BVH collision detection time taken: 62ms
GPU BVH:
GPU BVH build time taken: 174ms
GPU collision detected number is: 1754
GPU collision detected time used: 7 ms
GPU Naive:
GPU collision detected number is: 1754
GPU collision detected time used: 546 ms
CPU Naive:
CPU collision detected time used: 7154 ms
CPU collision detected number is: 1754
-------------------------------
Finish checking: 8.17685 seconds

run 2：

Start checking self-CD...
-------------------------------
CPU BVH:
CPU BVH build time taken: 212ms
CPU BVH collision detected number is: 1754
CPU BVH collision detection time taken: 62ms
GPU BVH:
GPU BVH build time taken: 91ms
GPU collision detected number is: 1754
GPU collision detected time used: 4 ms
GPU Naive:
GPU collision detected number is: 1754
GPU collision detected time used: 553 ms
CPU Naive:
CPU collision detected time used: 7465 ms
CPU collision detected number is: 1754
-------------------------------
Finish checking: 8.40536 seconds

run 3：

Start checking self-CD...
-------------------------------
CPU BVH:
CPU BVH build time taken: 211ms
CPU BVH collision detected number is: 1754
CPU BVH collision detection time taken: 61ms
GPU BVH:
GPU BVH build time taken: 89ms
GPU collision detected number is: 1754
GPU collision detected time used: 4 ms
GPU Naive:
GPU collision detected number is: 1754
GPU collision detected time used: 538 ms
CPU Naive:
CPU collision detected time used: 7616 ms
CPU collision detected number is: 1754
-------------------------------
Finish checking: 8.53671 seconds

实验结论